## Slide 1: Mapping Powerline RFI
What do you need?
How do you begin?
How do you analyze the results?
Follow up

## Slide 2: Is it Powerline Noise?
Characteristic 8 MS audio peaks – may be more than one. The noise may go away in wet weather when water fills in “microgaps.”
Buzzing sound on AM
Since the fundimental is at 120 Hz, the noise is strongest at low frequencies, e.g. the AM broadcast band and less at higher frequencies.
Resonant antennas will make the noise stronger on those frequencies for which they were designed. HF hunting is therefore done with non-resonant short loops or sticks.

## Slide 3: What Do you Need?
IC705 that includes CI-V S-meter export and GPS.
Quiet (RFI) vehicle.
RFI-quiet Windows laptop running W4DD software (Win10,11.)
Interconnecting cable with ferrites for RFI suppresson.
10 meter mobile antenna (e.g. hamstick.)

## Slide 4: Setting up the PC
Download the W4DD software (contact me)
Install the usb drivers from the Icom web site
You may need a Google account for MyMaps

## Slide 5
Win10 Laptop connected to IC705 with microUSB to USB cable

## Slide 6
10M Hamstick on three magnet mag mount (behind 2M/70 cm mag mount.

## Slide 7: Why 10M Mobile?
Powerline noise propagates down the power line.
This smears the noise signature at low frequencies and makes identification of a specific pole difficult.
28 MHz is sufficiently high in frequency to identify a cluster of suspect poles.
Haven’t tried 6M but I suspect similar behavior. Might be better.

## Slide 8
HF
VHF
HF VS. VHF Noise Profiles
Powerline
Noise Source

## Slide 9: How Do You Begin?
Take a partner with you – you concentrate on driving!
Identify an area of interest (beam headings, topography, etc.)
Use the AM mode on the IC705.
Note hills are strong RFI attenuators and the more beam headings affect the noise, the further away it is.
Start up the software and drive the area. A speed of 30 mph usually works well. Be aware of traffic!
When in doubt, cover more territory than you plan to.
Factor the weather into your plans…wet weather can make power line RFI go away! (the microgaps fill in)

## Slide 10
QTH
APPROX BEAM HEADING
Where Should I Look?

## Slide 11: Data in the RFI Data Folder
456 | 41.76333 | -70.0441 | 9 | 129 | 7
457 | 41.76331 | -70.044 | 10.5 | 129 | 7
458 | 41.76329 | -70.044 | 9 | 128 | 7
459 | 41.76328 | -70.0439 | 6 | 126 | 7
460 | 41.76326 | -70.0438 | 8 | 122 | 7
461 | 41.76324 | -70.0438 | 9.5 | 120 | 7
462 | 41.76323 | -70.0437 | 8.5 | 118 | 7
463 | 41.76321 | -70.0436 | 9.5 | 116 | 7
464 | 41.76319 | -70.0435 | 11 | 114 | 7
465 | 41.76317 | -70.0434 | 10.5 | 113 | 7
466 | 41.76316 | -70.0433 | 9.5 | 110 | 7
SAMPLE LATITUDE LONGITUDE S-MTR ELEVATION SATS

## Slide 12: Analyzing the Results
Import the data into Google My Maps
Set up the color scheme to make high noise areas clear…e.g. S1 – S8 in green, S9 in yellow, S9+ in orange, S9+20 in red, S9+30 in black.
Change the markers to plain circles for easier reading.
Identify power pole areas with high noise signatures.

## Slide 13: Importing the Data

## Slide 14: Select Data to be Mapped

## Slide 15: Customizing the Map for Analysis

## Slide 16: Select S-meter Color Coding

## Slide 17: Color and Symbol Selection

## Slide 18
Reviewing the detail with modified noise symbols

## Slide 19
Part of the plot showing high
noise in the vicinity of
Millstone Rd. and
Lund Farm Way

## Slide 20: Follow Up
Use VHF yagi and IC705 to locate specific pole.
Use ultrasonic dish to ID specific noisy component
  Candidates are line ties, transformers, lightning arrestors, cracked insulators…
Report problem to power company…state location, NOT pole number and get a case number.